## Slide 1: Reactive Real-time Scheduling Using Simulation-Optimization and Evolutionary Algorithms
Engelbert Pasieka, Sebastian Engell
CoDIT2024
Presented by Engelbert Pasieka

## Slide 2: Content
Introduction to scheduling
Simulation-optimization
A new approach to EA-based reactive real-time scheduling
Case study
Results
Conclusions & outlook

## Slide 3: Introduction to scheduling
Scheduling is a decision making process
It is used in many domains
  Production scheduling, airline scheduling, event scheduling
It decides on discrete degrees of freedom of the optimization problem, e.g.
  Allocation of entities to resources
  Splitting and merging of activities
  Sequencing and timing of activities
Scheduling in the process industry
  Batch production
  Multiple products
  Flexible plants
Harjunkoski, Maravelias, Bongers, Castro, Engell, Grossmann, Hooker, Méndez, Sand, Wassick: Scope for industrial applications of production scheduling models and solution methods,, Computers and Chemical Engineering, 2014, 62, 161-193
Notes: Airline scheduling combines flight scheduling, fleet assignment, crew scheduling.

## Slide 4: Simulation-optimization
Uses detailed simulation models to optimize real-world processes
Handles complex systems that are difficult to model analytically
Leads to more accurate predictions and better decision-making
Rigorous scheduling methods
Difficult to represent all features
Large computation times
Expert knowledge needed to maintain the solutions
Case Study: Industrial production plant (Crop protection)
Planning horizon of 1 month
~1000 batches aggregated into 28 campaigns
~20 minutes computation for a full simulation
Complex conditions and constraints
Heuristic rules for the discharging of tanks
Detailed representation of shift schedules and logistics

## Slide 5: Our Simulation-optimization framework
Production Plant
Allocation
Assign each (sub)order to a unit
E.g.:
Sequence
Set global priorities of each order
E.g.:
Batching
Start from a set of base orders
Repair algorithms needed
E.g.:
 | O1 | O2 | O3 | O4
Unit 1 | 1 | 3 | 2 | 7
Unit 2 | 5 | 6 | 4 | 3
4 | 2 | 1 | 3
 | O1 | O2 | O3 | O4
#Batches | 7 | 5 | 3 | 4
Scheduling System
Evolutionary Algorithm
Discrete-Event Simulation
Degrees
Of
Freedom
Model
Parameters
INOSIMCore
Extension
INOSIMCore
Extension
INOSIMCore
Extension
Parallelization of computation
Time
Objective
Problem Structure
Objective values
Scheduling decisions
Results
DEGREES OF FREEDOM
[1] C. Klanke and S. Engell, ”Scheduling and batching with evolutionary algorithms in simulation-optimization of an industrial formulation plant,” Computers & Industrial Engineering, vol. 174, Dec. 2022.

## Slide 6: Results for the example shown before
Evolution of the quality of the schedule for five runs of the algorithm
Partial schedule

## Slide 7: How to bring simulation-optimization to a real plant?
Schedules may become suboptimal or infeasible if disruptions occur
Minor disruptions
  Small impact on the schedule
  E.g., changes in start and end times
Core idea: Continuous improvement of schedules
The EA runs continuously
Model parameters and degrees of freedom of the EA are updated
  Periodic updates at fixed time points
  Event-driven updates after major disruptions
Updates of the degrees of freedom of the EA if the problem structure changes
Continuous generation of new schedules
Major disruptions
  Large impact that may lead to infeasibility
  E.g., rush orders, maintenance, failures
Arrival of new order P04
Notes: One of the main problems is that we have to deal with disruptive events. There are two kind of disruption. Minor disruptions usually don’t have a hugh impact on the predicited schedules. Events that fall under this category are changes in start and end times of operations, minor delays, and minor yield changes. One way to deal with these disruption is through periodic rescheduling. At fixed time intervals the scheduling system is update with the current plant state and reevaluated.

## Slide 8: Reactive real-time scheduling framework
SCHEDULING SYSTEM
Evolutionary Algorithm
PRODUCTION SYSTEM
Control Center
Starts the EA
Parametrizes the EA
Triggers updates
  Periodic
    E.g., delays
  Reactive
    Rush orders
    Maintenance
Production plant
Execution of schedules
Generates plant data
Decisions
Plant data
Modify genotypes
Order states → Sequence encoding =
Resource states → Allocation encoding =
Last population as initial solutions
Fix genomes of the last population
Inject new degrees of freedom into genomes
E.g.,
Discrete-event simulation
Decodes genomes
Evaluates schedules
Decisions & Predictions
Decisions & Predictions
Encode genomes
Genomes
Initial solutions
Genomes
Update trigger

## Slide 9: Pharmaceutical batch production process
[1] G. M. Kopanos, C. A. M´endez, L. Puigjaner, ”MIP-based decomposition strategies for large-scale scheduling problems in multiproduct multistage batch plants: A benchmark scheduling problem of the pharmaceutical industry,” European Journal of Operational Research,vol. 207, pp. 644?655, Dec. 2010.
Large batch scheduling problem
Multi-stage and multi-product plant
Eligibility constraints, changeovers
Degrees of freedom
Sequence of orders
The simulation handles the allocation heuristically
Objective
  Tardiness of orders
  Disruptions
  Rush orders and maintenance of machines

## Slide 10: Simulation results
Maintenance on machine “M1” for 3 h
Rush order “P01_Rush” of type “P01”
Duration change of maintenance on “M1” to 2.5 h
Rush order “P02_Rush” of type “P02”
Maintenance on machine “M3” for 3 h
Periodic Updates
1 hour of plant operation
On average every 2.5 minutes an operation happens
The optimizer runs continuously
Events that have occurred are fixed in the simulation
Events are handled in real-time
15 seconds response time after periodic updates
150 seconds response time after major disturbances
Current population is maintained
At 3255 seconds
At 3105 seconds
1h
2h
3h
4h
1h
2h
3h
4h

## Slide 11
Reactive Real-time Scheduling System
Untersuchung von Design-Parameter
Saubere Simulations- und Teststruktur
Updateintervall
Rückmeldeintervall
Reproduzierbarkeit
Initialisierung von Lösungen
Updates
Parameter
Kleinere Änderungen
Wie definiert?
Referenzlösung
Claire-Voyant
Beste letzte Lösung
Rechenzeit des EAs
Einfluss auf das System
Lösungsgüte
Widerstandsfähigkeit
Absichern der statistischen Signifikanz
Parametrierbar
Updates (Struktur und Zeiten)
Rückmeldungen
Aufträge
Störungen
Zielfunktion
(Model)
(Simulator)
Ziel
Untersuchung der System Eigenschaften
Leitfaden
Störungen
Delays
Ausfälle
Rush Order
Stochastisch
Deterministisch

## Slide 12: Abstract
We validate our approach using a multiproduct, multistage batch plant from the pharmaceutical industry, as in the work of Kopanos et al. [2], and demonstrate that it can generate high-quality solutions in the presence of new order arrivals and disturbances.
The results are compared with those provided by an idealized clairvoyant scheduler which has access to the full information before the schedule is computed.
The influence of the choice of the reaction time after a disturbance which involves a compromise between a fast reaction and better decisions in the immediate future is studied in detail.

## Slide 13: Schwerpunkt ESCAPE2025
Immediate Response Time
  Einfluss auf die Lösungsgüte
  Synchronisation statisch oder dynamisch?
Breite der Population
Steuerung der Population über die Distanz der Lösungen?
Wie viele Szenarien?
  Szenario 1: 4 Rush Order
  Szenario 2: …
  Stochastisch?
Claire-Voyant Vergleich

## Slide 14: Ergebnisse
Kopanos Case Study
  30 Aufträge
  Tardiness oder Tardiness + Avg. Earliness
  4 Rush Order -> Kann noch variiert werden
  300 Sekunden response time -> Variieren
Distance Measure
  Levenshtein Distance
  Umwandlung der Zeichenketten ineinander
Parameter Control

## Slide 15: Weitere Forschungsschwerpunkte (1/2)
Breite der Lösung des EAs kontrollieren -> GECCO 2025
  Vergleich: Enge Verteilung mit guter Lösung <-> Breite Verteilung mit schlechter Lösung
  Metrik erforderlich
    Hamming Distance -> nicht geeignet, da die Sequenz nicht berücksichtigt wird.
    Levenshtein Distance -> teilweise geeignet.
    N-Gram -> Gut geeignet, wenn modifiziert.
Ab wann ist eine Immediat Response notwendig -> Heuristiken als IR
  Quantifizieren der Störung
  Situationsbedingtes handeln
Nervousness
  E-Funktion über die Zeitachse als Penalty
  Multi-objective ansatz
Rolling Horizon
  Wie kann man Schedules bewerten

## Slide 16: Weitere Forschungsschwerpunkte (2/2)
Parameterstudien
Modellkonfigurationen

## Slide 17: Definition Stochastischer Störungen
Kleine Störungen
  Operationszeiten
    Dauer
    Startzeit
  Due Dates
Große Störungen
  Operationszeiten
    Dauer
    Startzeit
  Due Dates
  Ausfälle
    Maschinen
    Aufträgen
  Neue Aufträge
  Maintenance

## Slide 18: Untersuchung der Immediate Response Strategie
Anregung des Systems durch große Störungen
  N neue Aufträge mit engen Due Dates zur gleichen Zeit (N= 1, …, 5)
  Einfluss auf das System
    Tardiness
    Nervousness
  Teststruktur:
    Start mit einer guten Lösungen
    Das System mit Störungen anregen
  Ziel
    Systemeigenschaften: Anzahl Störung <-> Einfluss <-> Dauer der Konvergenz
    Zusammenhänge: Tardiness <-> Earliness (Slack) <-> Einfluss der Störungen
    Lösungsgüte
    Konvergenz
    Untersuchung von Paramtern:
      Größe der Population, Rückmeldeintervall, Earliness, Slack, Konvergenz, Nervousness

## Slide 19: Design of Experiments
Einflussgrößen Systemgrößen Objectives
Störungen
Populationsgröße
Initiallösung
Updateintervalls
Performanz
Konvergenz
Widerstand
Impact
Tardiness
Nervousness
Earliness
Tardiness
Slack
Anzahl
Art
Zeitpunkt
Claire-Voyant

## Slide 20: Untersuchungen
Einfluss der Störungen auf die Performanz und Kovergenz
  Quantifizierung der Störungen?
  (Bei Delays wichtig: Ab wann ist eine Immediate Response notwendig?)
Einfluss der Populationsgröße auf die Widerstandsfähigkeit und Kovergenz
Einfluss der Initiallösung auf die Widerstandsfähigkeit und Kovergenz
  Earliness, Slack
Entwicklung der Nervousness und Tardiness (Multiobjective Ansatz)
  Abweichungen der Lösungen durch Vergleich der Reihenfolgen der Operationen
  z.B.: M1: [P1,P2,P3,P4] M2:[P1,P2,P3_Rush, P3, P4]
    Jede Abweichung erhöht die Tardiness
    Aufsummieren der Abweichungen
    Parallel zur Tardiness Plotten
Einfluss der Earliness auf die Widerstandsfähigkeit und Kovergenz
  Absorbtionsfähigkeit des Systems
  Wieviele Störungen verkraftet das System?
Einfluss des Updateintervalls auf die Lösungsgüte und Konvergenz

## Slide 21: Start mit Initiallösung:
2 Rush Order
4 Rush Order

## Slide 22: PaperCept Conference Management System
I hope you're doing well. We are excited to announce that submissions are now open for two special issues dedicated to CoDIT 2024. Through this email, we strongly encourage you, as an author of a selected paper presented at the IEEE/IFAC CoDIT 2024 (https://codit2024.com/),to submit an extended version of your work.
The CFP for the two special issues are available here:
Optimization and Engineering Journal (Impact Factor:2.0) (Deadline 15. Nov)
https://link.springer.com/collections/fbjebdiaje
RAIRO - Operations Research (Impact Factor: 1.8) (Deadline 15. Dez)
https://www.rairo-ro.org/news/287-call-for-papers-special-issue-on-innovative-approaches-in-decision-and-optimization-theory-and-applications-perspective-codit-2024
Additionally, we will soon share the CFPs for two more special issues.

## Slide 23: Untersuchung des Updateintervalls
Änderung der Operationszeiten
  Annahme: Updateinterval proportional zur durschnittlichen Zeit zwischen Operationen
  Ist die Annahme gerechtfertigt?
Änderung der Modelle
  2X2, 3X3, 4X4 (Maschinen X Stages)
Anzahl der Orders und Störungen
Sind die Ergebnisse der Untersuchungen der Immediate Response Strategie übertragbar?

## Slide 24: Conclusions and outlook
A new approach to real-time scheduling is proposed
Based on simulation-optimization with detailed simulation models
Updates the simulation model and the genotypes of the EA and continuously runs the optimization
The performance was demonstrated for a complex pharmaceutical production example
Outlook
Rolling-horizon approach
Reducing scheduling nervousness

## Slide 25: Anforderungen an die Simulation ausarbeiten
Initialisierbar
Parametrisierbar
Dynamische Rezepte
Muss ein neuer Simualtionsansatz entwickelt werden?
Stateful Discrete Event Simulations

## Slide 26: Thank you!

## Slide 27: Backup

## Slide 28: Results of different simulation runs